## NEMA Design

The National Electrical ManufacturerAssociation sets standards for motors in the US. The IEC has similar standards for Europe.

DESIGN A, B, C, D - for AC MOTORS 
NEMA has standard NEMA motor designs of various torque characteristics to meet the various requirements posed by different application loads. The design "B" is the most common design. (See chart for characteristics of each design.)

| NEMA DESIGN | STARTING TORQUE | STARTING CURRENT | BREAK- DOWN TORQUE | FULL LOAD SLIP | TYPICAL APPLICATIONS |
| --- | --- | --- | --- | --- | --- |
| A | Normal | High | High | Low | Mach. Tools, Fans |
| B | Normal | Normal | Normal | Normal | Same as Design "A" |
| C | High | Normal | Low | Normal | Loaded compressor Loaded conveyor |
| D | Very high | Low | ------- | High | High Punch Press |

DIMENSIONS
NEMA has standard frame sizes and dimensions designating the height of the shaft, the distance between mounting bolt holes and various other measurements. The integral AC motor NEMA sizes run from 143T- 445T, and the center of the shaft height in inches can be figured by taking the first two digits of the frame number and dividing it by 4. 
The fractional horsepower motors, for which NEMA spells out dimensions, utilize 42, 48 and 56 frames whose shaft height in inches is figured by dividing the frame number by 16.

Marcus O. Durham, PhD, PE

10/25/05						( ( (